## Slide 1
Out of Sight, Out of Mind: Using visual perception to probe subtle effects of mild traumatic brain injury on cortical physiology.
Indiana Clinical and Translational Sciences Institute
Elizabeth Frazier
PhD Student: Purdue University, Weldon School of Biomedical Engineering
Co-Authors: Anne Sereno, PhD; Maria Dadarlat, PhD
2023 Annual Meeting

## Slide 2: Results | A behavioral task to probe post-mTBI visual deficits
Traumatic brain injury (TBI) is a leading cause of death and disability.
Mild TBI (mTBI) is particularly diverse in functional deficits and patient prognosis.
Many mTBI patients suffer from
visual dysfunctions and visual acuity loss.
Neuropathology of mTBI disrupts cortical circuitry.
Established framework to bridge visual deficits and cortical circuitry changes following mTBI.
Developed a novel two alternative forced choice (2AFC) task to probe perception of complex global motion stimuli in mice, compatible with head-fixation for in vivo electrophysiology
Validated parameters to reliably generate mTBI in mice using a controlled cortical impact (CCI)

## Slide 3: Methods | 2AFC task overview and mTBI validation
Created using Biorender.
Controlled Cortical Impact Setup
2AFC Task: Mice report global motion of a random dot kinematogram (RDK) with a wheel turn
Sample Psychometric Data
mTBI: Mice receive a mild impact to skull over primary visual cortex
RDK Coherence
Impactor Parameters:
3 m/s tip velocity
0.8 mm depth
180 ms dwell time
3mm plastic tip
2AFC Task Setup

## Slide 4: Future Work | Next steps and patient implications
Acute, in vivo electrophysiology
Overall Objective | Correlate physiological outcomes post-mTBI to simple, visual behavior outcomes.
Immediate Next Steps | Bridge behavior with electrophysiology
Acutely implant recording electrodes into the cortex of awake, behaving mice performing 2AFC task
Assess changes in behavior (speed/accuracy) and physiology (RDK-evoked responses/functional connectivity) following mTBI
Human Translation | Improve mTBI diagnosis and monitoring
Facilitate estimation of latent physiological changes after mTBI using performance on simple behavioral tasks
Improve prediction of mTBI prognosis
Translate 2AFC task to an easily administered, cost-effective tool to improve diagnosis and rehabilitation of mTBI patients

## Slide 5: Grant Acknowledgement
“This project was funded with support from the Indiana Clinical and Translational Sciences Institute which is funded in part by Award Number UL1TR002529 from the National Institutes of Health, National Center for Advancing Translational Sciences, Clinical and Translational Sciences Award. The content is solely the responsibility of the authors and does not necessarily represent the official views of the National Institutes of Health.”
Thank you for your attention!